## Slide 1: Orbit & Sensor Evaluation
500 km Sun-Sync Terminator Orbit + 1 km Push-Broom Imaging
Durgesh • 22 Sep 2025

## Slide 2: Mission Concept
500 km sun-synchronous terminator orbit
Push-broom scanner with 1 km swath
Targeted Earth-observation trade study

## Slide 3: Orbital Parameters
Altitude: 500 km
Period: ~94.62 minutes
Orbits per day: ~15.22
Speed: ~7.613 km/s
T = 2π√((Re + h)^3 / μ)

## Slide 4: Sun-Sync Design
Nodal precession ≈ 0.98565°/day
Inclination ≈ 97.40° (retrograde)
Terminator orbit for constant lighting

## Slide 5: Swath Geometry
Swath: 1 km at 500 km altitude
FOV ≈ swath / h = 1 km / 500 km = 0.002 rad ≈ 0.115°

## Slide 6: Optics & Detector
GSD = swath / N
f = (h · p · N) / swath
IFOV = p / f

## Slide 7: Worked Examples
5 µm, 1024px → GSD 0.9766 m, f=2.56 m, IFOV=0.403″
5 µm, 2048px → GSD 0.4883 m, f=5.12 m, IFOV=0.201″
10 µm,4096px → GSD 0.2441 m, f=20.48 m, IFOV=0.101″

## Slide 8: Along-Track Sampling
Ground speed v ≈ 7.613 km/s
Line rate = v / GSD
Example: GSD 0.488 m → 15.6 kHz

## Slide 9: Coverage & Revisit
Area/day ≈ 610,000 km²
Earth area ≈ 510×10^6 km²
Full global cover ≈ 836 days
Constellations for practical revisit

## Slide 10: Trade-Offs & Conclusions
Large optics needed for long focal lengths
High line rates → fast detectors (TDI/CMOS)
Sub-meter GSD demands tight stability
Off-nadir improves revisit at cost of distortion